## Slide 1
Washing
Machine
Microcontroller
7 Seg Display
Coin Selector
Button
Vending Washing Machine – Block Diagram

## Slide 2
Washing Machine :
  This acts as both input and output to uC.
  Based on Input coin value, the modes needs to selected
  Possibility of 3 modes
    15 Min [Coin value 1]
    30 Min [Coin value 2]
    45 Min [Coin value 3]
  Feedback on each state is needed
    Idle
    Running
    Done

## Slide 3
7 Seg Display :
On power on display based on current state
Idle State
  Display ‘rdy’
  On coin insertion , display countdown timer of 20 sec
Running state
  Display countdown timer based on mode selected
Done state
  Display ‘ovr’ for ~10 sec and then change to ‘rdy’
Reset state
  Only used by machine owners
  On long press display total coin collected values ‘val ’ / ‘000’ , alternately
  On press single click value reset to zero , display ‘000’ for 3 sec and change to ‘rdy’

## Slide 4
Coin Selector:
It gives the impluses based on the types of coin
Currently we are sticking to 1 value of coin i.e 1 Dhiram
It gives if a coin is valid
In case of valid value is set to 1
In case of invalid coin is rejected

## Slide 5
Button:
Not exposed to normal users, only for machine owners
Press long ~5 sec to display total collected coin value
Then a single press to reset the value

## Slide 6
Microcontroller:
Mainly works on 4 state
  Idle -> default state on power on of fresh start. Ready to accept new coins.
  Running -> currently running mode [15,30,45 ]
  Done -> after a completion of wash cycle
  Reset -> Coin value reset [used only by owners]
When in Idle state, based on feedback of coin selector on valid coin and number of coins taken , sets the mode of operation [15,30,45]
Once mode is selected, trigger a start pulse to washing machine. On receiving the feedback from washing machine on start of run , change the state to “Running”, send the value of countdown timer to display
Once washing cycle is completed , send stop pulse to washing machine and on receiving the feedback of stop signal change state to “Done”
On pressing long for ~5sec , Display the total collected coin value
One more press then , reset the coin value and state changed to “Idle” and display ‘rdy’
Save the following parameters always in eeprom
  Current state
  Current mode
  Coin value collected in total
  Countdown timer value